## Slide 1: UTA EE Labs
Controlling your Arduino with Bluetooth
IEEE 802.15. 4

## Slide 2: Why the Name Bluetooth
King Harald “Bluetooth” Gormsson was viewed as a great uniter.
He ate lots, and lots of blueberries.
Bluetooth tech seeks to “unite” devices.
Bluetooth symbol is his initials in Nordic Runes.

## Slide 3: Differences in Bluetooth classic, 4.2 and 5.0

## Slide 4: BLE Versus Bluetooth Classic

## Slide 5: Modulation: Frequency Shift keying
Data
Carrier Frequency
Modulated Carrier

## Slide 6: HC-05 & HM-19 Bluetooth module
HC-05
  Uses Bluetooth 3.0
  iPhone does not support BT 3.0
HM-19
  Uses Bluetooth 5 and 4.2
  Most modern phones support Bluetooth 4.0 and higher

## Slide 7: HM-19 Pinout
TI CC2640R2F Bluetooth Chip
Antenna is a trace on the PCB
3.3V Logic to RX Pin. Must use a voltage divider to lower 5V logic from Arduino.

## Slide 8: Let’s Create
Cathode is on the right
Notice the 200 and 300 Ω resistors make a voltage divider because the Arduino has 5V logic but the HM-19 takes 3.3V logic

## Slide 9: Let’s Create
Insert the HM-19 Module
Turn on the Oscilloscope and measure the RX on channel 1 and the TX on channel 2 so you can see if both the TX and RX are working.

## Slide 10: Let’s Code
Download SoftwareSerialExample.ino from the UTA EE Lab Git hub page:
https://github.com/EELabMan/Bluetooth/blob/main/BT_AT_Commands/BT_AT_Commands.ino
Upload this to the Arduino

## Slide 11: AT COMMANDS for HM-19
Open the serial monitor and enter the following AT Commands
AT : Check the connection. Should return OK AT+NAME? : See default name AT+ADDR? : Returned the device MAC Address AT+VERS? : See firmware version AT+BAUD? : See baudrate
Many more on the datasheet.

## Slide 12: Set a new Name for the HC-19
Type AT+NAMEXXX - XXX is any short name you want.
Should return OK
Type AT+NAME? to confirm new name.

## Slide 13: Add the Dabble Library to Arduino
Download the Dabble Arduino Library ZIP file from our GitHub page.
Place it in the Documents\Arduino\libraries folder. Do not unzip the zip file.
In the Arduino IDE go to Sketch -> Included Library -> Add ZIP Library.
Select the Dabble-master.zip file from the Documents\Arduino\libraries folder.

## Slide 14: Open the Sketch
File -> Examples -> Dabble -> 02.Uno Nano Mega
Select 01.LedBrightnessControl
Upload to your UNO.

## Slide 15: Install Dabble on your smart phone
Dabble is available for the Android user functioning on Android version 5.0.0 and above.
It is compatible with iPhone, iPad, and iPad touch and requires iOS 12.2 and above

## Slide 16: Open Dabble and connect
Open dabble and select the connection icon
Find your BT device and select

## Slide 17: Open the LED Brightness Control
Open the serial monitor in the Arduino IDE
Select pins 5, 6, 9 and 11 on the Dabble app to control the LED’s.

## Slide 18: Open the Sketch
Disconnect from Dabble on your phone first.
Download from GitHub Terminal_Voice.ino
Upload to your UNO.
Open Dabble and connect to BT.
Open terminal
Open the serial Monitor in the Arduino IDE
Press the microphone on Dabble and say “Turn on the blue LED”
Depending on your voice assistant, you may need to change the Arduino code.
Try “all on” and “all off”
Type a message in the Arduino Serial Monitor to send to Dabble

## Slide 19: Dabble GamePad
Download Gamepad_LED.ino from GitHub and upload it to your arduino
Open Dabble and connect again.
Examine the code while pressing the buttons.

## Slide 20: Phone Sensors
A lot of neat things your phone can do. We’ll play with the accelerometer.
Download Accelerometer_LED.ino from GitHub.
Upload to the Arduino and open the serial monitor.
Open Dabble and select Phone Sensors.
Switch the Accelerometer on and rotate your phone.
Try editing the code to light up the LEDS in order as you twist your phone

## Slide 21: UTA EE Lab Workshops
Hope you enjoyed the
Workshop